CHITRANJALI STUDIO

(A Unit of Kerala State Film Development Corporation Ltd)

Thiruvallam, Thiruvananthapuram-27.

Phone: (0471) 2381450,51,52,2380946

E-mail: chitranjalistudio@yahoo.com

No:08/CS/MM/DI/2017-18					                     22/05/2017

Quotation Notice

Sealed quotations are invited from OEM/authorized dealers for the supply and installation of Multi Channel Home Theatre Processor-1 No., Three Way Active Loudspeaker with Floor Stand- 2 Nos..

Last date of receipt of quotation 		:   06/06/17 - 3 PM

For details visit  www.ksfdc.in or contact 	:    9961968135.

Studio Manager i/c.

CHITRANJALI STUDIO

(A Unit of Kerala State Film Development Corporation Ltd)

Thiruvallam, Thiruvananthapuram-27.

Phone: (0471) 2381450,51,52,2380946

E-mail: chitranjalistudio@yahoo.com

No:08/CS/MM/DI./2017-18						              22/05/2017

Notice Inviting Quotations for Supplying Multi Channel Home Theatre Processor- 1 No., Three Way Active Loudspeaker with

Floor Stand-2 Nos.

1)	Sealed quotations are invited from original equipment manufacturers/authorized dealers for Multi Channel Home Theatre Processor-1 No., Three Way Active Loudspeaker with Floor Stand-2 Nos. the following specification.

Item No.1: Multichannel Home Theatre Processor – 1 No.

Description	:  Multichannel Processor

Features	:  HDMI 1.4 (1080P), 32 bit DSP decoding Dolby.

Terminal	:  Minimum Requirement

HDMI in-4, HDMI out -2

Digital Coaxial: 2 in; Digital Optical:2 in;

Bluetooth digital: 1 in;

Analogue Audio Inputs: 4 Sets

7.2 Line out, Subwoofer Line out (after Dolby, DTS decoded);

Item No.2 : Three Way Active Loudspeaker with Floor Stand- 2 No.

Description		:   Active Loudspeaker – three way with floor stand

Transducer Section	:  Lf Transducer – 1” ( 1 No.)

Mf Transducer – 4” (1 No.)

Hf Transducer – 8” ( 1 No.)

SPL 115 dB

Frequency Response – 40 Hz to 20 kHz (+/- 3 dB)

Requirement		:   Minimum Requirement

Amplifier type Class H

Amplifier Power requirement – LF 150 W, MF 75 W and HF

75 W.

Maximum THD 0.1%

Connectivity Balance XLR socket

Floor Stand

2)	Item has to be delivered, installed, tested and commissioned at Chitranjali Studio, Thiruvallam, Thiruvananthapuram.

3)	2.5% of quoted rate may be offered as EMD along with quotation by way of DD payable to KSFDC Ltd at Thiruvananthapuram.

4)	Minimum 1 year warranty may be provided.

5)	Original equipment manufactures or their appointed dealers only are eligible to quote.

6)	The selected OEM/Dealer should deposit 5%  of the quoted amount with KSFDC on security deposit to cover the clause of warranty during defect  liability period.  If needed, EMD amount shall be adjusted against Security Deposit and balance amount only to be remitted.

7)	The last date of receipt of quotation is 3 PM on 06/06/17.  The quotations will be opened on the same day at 4 PM in the presence of available suppliers.

8)	KSFDC reserves the right to reject any or all quotations without assigning any reason whatsoever.

9)	Delivery and completion of period of installation will be 7 days from the date of  issue of letter accepting the quotation.

10)	Payment will be against supply and installation of items covered under quotation.

11	If needed prior demonstration of item before acceptance of  quotation may be arranged by the quotationer.

12)	A copy of this quotation notice may be enclosed with quotation duly signed and affixed with seal for the acceptance of the terms & conditions by the quotationer.

13)	Quotation may be submitted on plain paper/letter head with all inclusive rates, specifications, warranty period, etc.  Product catalogue may be attached.

14)	List of clients may be enclosed.

15)	Quotation shall be valid for 90 days.

16)	Quotation in sealed cover superscripted “Quotation for Item No.1-Multichannel Home Theatre Processor – 1 No. with Three Way Active Loudspeaker with Floor Stand- 2 Nos.” and may be sent to Studio Manager i/c., Chitranjali Studio, Thiruvallam, Thiruvananthapuram-27.

Sd/-

Studio Manager i/c.